## Slide 1
The
European
Extremely Large Telescope

## Slide 2: The E-ELT
40-m class telescope: largest optical-infrared telescope in the world.
Segmented primary mirror.
Active optics to maintain collimation and mirror figure.
Adaptive optics assisted telescope.
Diffraction limited performance.
Wide field of view: 10 arcmin.
Mid-latitude site (Armazones in Chile).
Fast instrument changes.
VLT level of efficiency in operations.

## Slide 3: The Science
Contemporary science:
Exoplanets: radial velocity detections, direct imaging, transit spectroscopy, proto-planetary disks
Fundamental physics: GR in the strong field limit, variation of fundamental constants, expansion history of the Universe
Resolved stellar populations: beyond the Local Group
The physics of high-redshift galaxies
…and much more!
Synergies with other top facilities:
ALMA
JWST
LSST and other survey telescopes
SKA
Discovery potential:
Opening new parameter space in terms of spatial resolution and sensitivity
SKA
JWST
ALMA
LSST

## Slide 4: The E-ELT Project
Top priority of European ground-based astronomy (on Astronet and ESFRI lists).
Cerro Armazones in Chile selected as the E-ELT site in April 2010.
Detailed Design Phase completed in 2011. Construction Proposal published in Dec 2011.
Instrument Roadmap (Nov 2011): 2 first-light instruments + plan for 1st generation.
Project fully approved in Dec 2012.
Construction started in 2013.
Start of operations early next decade.
Construction cost: 1083 M€ (including first-light instrumentation).

## Slide 5: The Telescope
Nasmyth telescope with a segmented primary mirror.
Novel 5 mirror design to include adaptive optics in the telescope.
Classical 3mirror anastigmat + 2 flat fold mirrors (M4, M5).
M1 (seg): 39.3 m
M2: 4.2 m
M5 (TT): 2.6x2.1 m
Nasmyth focus
M3: 3.8 m
M4 (AO): 2.4 m
Two instrument platforms nearly the size of tennis courts can host 3 instruments each + Coudé lab.
Multiple laser guide stars, launched from the side.
Nearly 3000 tonnes of moving structure.

## Slide 6: The Mirrors
M1: 39.3 m, 798 hexagonal segments of 1.45 m tip-to-tip: 978 m2 collecting area
M4: 2.4 m, flat, adaptive 6000 to 8000 actuators
M5: 2.6 x 2.1 m, flat, provides tip-tilt correction

## Slide 7: The Dome
Classical design.
Diameter = 86 m, height = 74 m.
~3000 tonnes of steel.
Fully air-conditioned and wind shielded.

## Slide 8: The Instruments
The telescope can host eight instruments.
2007 – 2010: eight instrument and two adaptive optics module concept studies were conducted by the community.
Instrument Roadmap (2011):
  Following recommendations by the E-ELT Science Working Group and ESO's Scientific Technical Committee two first-light instruments have been identified: a diffraction-limited near-infrared imager and a single-field near-infrared wide-band integral field spectrograph.
  The next group (ELT-3, 4 and 5) has been broadly identified as covering the mid-infrared, as well as multi-object and high-resolution spectroscopy.
  Planet camera and spectrograph on separate track.
  Flexibility is maintained by including an as yet unspecified instrument.
  All concept studies remain in the pool of possible instruments.

## Slide 9: Instrument Roadmap

## Slide 10: The Site
Following an extensive site testing campaign, involving several sites in Chile, Morocco, the Canary Islands, Argentina, Mexico, etc, ESO Council selected Cerro Armazones as the E-ELT site.
Selection criteria: impact on science, outstanding atmosphere, but also construction and operations logistics (roads, water, electricity, nearby cities, ...).

## Slide 11
Armazones
Paranal

## Slide 12: More information
The science users web pages:
www.eso.org/sci/facilities/eelt
The E-ELT Construction Proposal:
www.eso.org/sci/facilities/eelt/docs/eelt_constrproposal.pdf
The E-ELT Science Case:
www.eso.org/sci/facilities/eelt/science/doc/eelt_sciencecase.pdf
The E-ELT Design Reference Mission:
www.eso.org/sci/facilities/eelt/science/doc/drm_report.pdf
The public web pages:
www.eso.org/public/telesinstr/eelt.html
Brochures, Posters, etc:
www.eso.org/public/products/brochures/
Gallery:
www.eso.org/public/images/archive/category/eelt/