## Slide 1: High-Speed, Photon Counting CCD cameras for Astronomy
14 October 2009: ESO, Scientific Detectors Meeting
Craig Mackay,
Institute of Astronomy
University of Cambridge.
Notes: <number>

## Slide 2: Introduction.
14 October 2009: ESO, Scientific Detectors Meeting
This presentation describes results obtained with electron multiplying CCDs (L3CCDs) manufactured by E2V Technologies Ltd.
Cameras intended for high-speed photon counting applications are very different beasts from standard slow-scan camera systems, and a very different approach to their design is essential.
Things are made easier because of the availability of extraordinarily high performance devices used by the digital camera industry.
30 MHZ 14-bit DCS/ADC processor for EMCCD cameras.
Notes: <number>

## Slide 3: EMCCD Issues.
14 October 2009: ESO, Scientific Detectors Meeting
It is widely believed that electron multiplying CCDs suffer from two principal problems: clock induced charge and the quantum efficiency degradation that comes from the multiplying process.
The QE problem is easily overcome if the photon rates are low enough so that a level of one photon per pixel per frame is seldom achieved. Thresholding the data and setting each pixel to 0 or 1 recovers all the lost quantum efficiency.
This is most easily achieved at high frame rates provided there are no other reasons to read out more slowly.
The principal reason for not reading out unnecessarily is the clock induced charge (CIC).
Notes: <number>

## Slide 4: Clock Induced Charge (CIC).
14 October 2009: ESO, Scientific Detectors Meeting
Clock induced charge (aka spurious charge) is caused when a CCD is clocked into inversion (see Janesick’s CCD bible). Fast clock rise times, slow clocking and high clock swings amplitudes all make CIC worse.
Photon counting systems work with extremely low signal levels and so parallel clock swings can be reduced greatly.
Commercial cameras must be able to function satisfactorily with unity gain. This requires higher clock swings and therefore much greater CIC.
Arranging the clocks to work as fast as possible and then trimming the rise time of the clock pulses as much as possible so that the charge is still transferred properly is the best strategy for minimising CIC.
Notes: <number>

## Slide 5: Test Results: E2V CCD201.
14 October 2009: ESO, Scientific Detectors Meeting
Results with the E2V Technologies Ltd CCD 201 have been excellent.
Our camera runs up to 30 MHz pixel rate with double correlated sampling and 14 bit digitisation.
Although the CCD 201 is specified at a maximum parallel transfer rate of 900 kHz we have been running it happily at 1.8 MHz.
The maximum pixel rate suggested is 20 MHz but again we have been running faster at 26 MHz.
We see negligible
clock induced
charge in the
parallel direction.
This image shows
the test chart
arrangement with
full serial overscan.
Notes: <number>

## Slide 6: Test Results: E2V CCD201.
14 October 2009: ESO, Scientific Detectors Meeting
This plot shows the natural log of the event distribution in the image (upper) area of the CCD and the overscan (lower) region. These plots determine the gain.
The steeper slope gives a gain of ~1/sqrt of the image area showing the events must be generated in the multiplication register.
The choice of threshold can minimise noise or CIC events contaminating at the expense of loosing photons.
For our cameras, we get 1% of pixels/frame affected with a threshold of 0.07-0.1 e (loosing 6-9% of photons) and 0.1% pixels/frame with 0.1-0.2 e threshold (loosing 9-20%).
Significant differences between CCDs/read-speed/electronic setups.
Notes: <number>

## Slide 7: Test Results: E2V CCD201.
14 October 2009: ESO, Scientific Detectors Meeting
Sequence shows images collected at 26MHz pixel rate, 24 fps, at a peak signal flux of 0.2 photons/pixel/sec detected.
Final frame of the sequence shows 20 secs of data averaged so it has a peak signal of 10 photons/pixel.
Notes: <number>

## Slide 8: Serial Clock Induced Charge.
14 October 2009: ESO, Scientific Detectors Meeting
Our tests indicate that almost all the CIC arises in the multiplication register as a result of the amplitude and trimming of the high-voltage clock.
We use a pulsed clock which comes out to be sort of square wave until we trim it back to round off all the edges. This is difficult since what the oscilloscope shows is only vaguely related to what is going on inside the CCD.
The tracks between the clock board and the CCD inside the cooled head must be setup as a transmission line with careful impedance matching to the capacitance of the specific clock been driven. This minimises reflections and it is the highest voltage on the high-voltage clock phase line that largely determines serial CIC.
Notes: <number>

## Slide 9: Clock Induced Avalanching.
14 October 2009: ESO, Scientific Detectors Meeting
There is an additional problem with the multiplication register.
When operating with high levels of gain (> 5000) the avalanche effect is working near breakdown and pixels that are already at a high signal level find that it is possible for additional electrons to be dislodged during the amplification process.
This can be seen even at very low signal levels if the gain is high enough.
There is no benefit to increasing the gain unnecessarily. Reasonable electronics design will give a read noise (unity gain) of ~70-100 e RMS. Gains of ~2000 will give an SNR ~ 20.
Notes: <number>

## Slide 10: Clock Induced Avalanching.
14 October 2009: ESO, Scientific Detectors Meeting
These are averaged images of a very faint flat field with the multiplication set to ~12000.
The effective gain progressively increases along the multiplication register because of enhanced avalanche multiplication.
This becomes an issue with gains about 3000-5000.
Notes: <number>

## Slide 11: Lucky Imaging Results.
14 October 2009: ESO, Scientific Detectors Meeting
Thresholding is essential to recover full QE with EMCCDs. It is also essential at low photon rates to ensure that read noise does not set the background noise.
Lucky Imaging uses fast frame rate photon-counting cameras to freeze the image motion due to atmospheric turbulence. A compact reference star allows the sharpest images to be identified. They are shifted and added to give a longer exposure image.
On 2.5m ground-based telescopes it is routinely practical to get Hubble resolution with 10-30% image selection, depending on conditions.
Notes: <number>

## Slide 12: Lucky Imaging Results.
14 October 2009: ESO, Scientific Detectors Meeting
Einstein Cross Gravitational Lens. HST (left), Lucky on the right.
Resolution with Lucky on 2.5m is better than Hubble as HST is significantly undersampled.
The lens components change relative brightness on short time scales (months>>years) because of microlensing by objects in the core of the lensing galaxy.
Notes: <number>

## Slide 13: Lucky plus Low-Order AO.
14 October 2009: ESO, Scientific Detectors Meeting
The chance of a sharp image with telescopes >2.5m quickly becomes negligible.
Can remove the largest scales of turbulence with a low-order adaptive optics system in front of a Lucky Camera.
This was demonstrated on the
Palomar 5m telescope
and produced the highest
resolution images ever
taken, with 35 milliarcsecs
resolution in I-band.
The first image shows the
0.65 arcsec seeing that night
and the second shows Lucky
plus PALMAO, low order AO.
Notes: <number>

## Slide 14: Lucky plus Low-Order AO.
14 October 2009: ESO, Scientific Detectors Meeting
Curvature wavefront sensors are ~10x more sensitive than Shack-Hartmann sensors for low-order AO.
Combining images from either side of the pupil plane allows the wavefront errors to be established.
By using an EMCCD photon-counting at high speed, highly efficient systems may be built that may be dynamically reconfigured as the conditions change.
Much more sensitive, reliable and cheaper than APD solutions.
Simulations by Olivier Guyon (Subaru, Hawaii) shown here, and predict we can use reference stars as faint as 18.5 mag, so able to find such stars nearly everywhere.
Notes: <number>

## Slide 15: Lucky plus Low-Order AO.
14 October 2009: ESO, Scientific Detectors Meeting
On the VLT, such a system should deliver images with ~25 milliarcsec resolution, and ~20 milliarcsec on Keck or GTC.
Lucky also gives a wide isoplanatic patch size.
We have built a quad 1024x1024 EMCCD camera that produces >200MBytes/sec continuously and allows wide field Lucky.
Our latest results suggest an isoplanatic patch size of >3 arcmin should be possible.
Notes: <number>

## Slide 16: Conclusions.
14 October 2009: ESO, Scientific Detectors Meeting
Electron Multiplying CCDs have a great potential for high-speed astronomy such as time resolved photometry or spectroscopy (for example, 1000 point photon-counting spectroscopy at >1KHz).
When used thoughtfully they are easy to work with and can produce interesting and unique results.
Notes: <number>

## Slide 17: Instrumentation Group Institute of Astronomy University of Cambridge, UK cdm@ast.cam.ac.uk
14 October 2009: ESO, Scientific Detectors Meeting
Notes: <number>